## Slide 1
Smart Home Security & Intruder Detection System
Design & Simulation Using Combinational Logic
DDCA — Module 2 Combinational Logic • K-Maps • Adders • ALU
1/9

## Slide 2
1. Combinational Logic — The Core Idea
Output depends only on the current inputs — there is no memory.
INPUTS
Sensors and switches provide binary signals: 0 = inactive, 1 = active.
LOGIC
AND, OR, NOT, XOR and other gates process the current inputs.
OUTPUT
The system immediately decides: SAFE, ALERT or ALARM.
Door = 1
Motion = 1
Alarm = 1
Key property: no previous state is stored. Change the inputs → the output can change immediately.
2/9

## Slide 3
2. K-Maps — Simplifying the Logic
Fewer gates → simpler, faster, cheaper and lower-power hardware.
Why simplify?
Reduce the number of gates and connections while keeping the same required output.
K-Map method
1. Build the truth table 2. Place 1s in the K-map 3. Group adjacent 1s in powers of 2 4. Write the simplified Boolean expression
Worked example
Suppose Alarm = Door·Motion + Window·Motion. Factor Motion: Alarm = Motion(Door + Window).
D · M
W · M
OR
Simplified form: M(D + W) This can reduce the gate count and wiring.
3/9

## Slide 4
3. Security System Inputs & Truth-Table Logic
Convert real security conditions into binary variables.
D — Door
1 = door open 0 = closed
W — Window
1 = window open 0 = closed
M — Motion
1 = motion detected 0 = none
A — Armed
1 = system armed 0 = disarmed
Intrusion = D + W
ALARM = A·(D+W+M)
Buzzer
Example: if the system is armed (A=1) and either the door, window, or motion sensor is active, the alarm output becomes 1.
4/9

## Slide 5
4. Half Adder & Full Adder
Arithmetic circuits show how combinational logic can perform binary addition.
Half Adder
Inputs: A, B Sum = A XOR B Carry = A AND B Used for adding two single-bit numbers.
Full Adder
Inputs: A, B, Cin Sum = A XOR B XOR Cin Cout = AB + Cin(A XOR B) Handles an incoming carry.
A
B
Cin
Sum
Cout
0
0
0
0
0
0
1
0
1
0
1
1
0
0
1
1
0
1
0
1
1
1
1
1
1
Security connection: The same AND/OR/XOR building blocks used by adders are used to combine sensor decisions.
5/9

## Slide 6
5. Ripple-Carry Adder — Chaining Full Adders
A multi-bit adder is built by connecting the carry-out of one stage to the carry-in of the next.
Full Adder Bit 0
C
Full Adder Bit 1
C
Full Adder Bit 2
C
Full Adder Bit 3
Example: 1011 + 0110 = 10001 Each full adder calculates one bit and passes the carry forward. The same modular design idea is useful when building larger digital systems.
6/9

## Slide 7
6. Smart Home Security — Complete Combinational Design
A simple decision network for door, window, motion and arming status.
Door D
Window W
Motion M
OR Intrusion
AND with Armed
ALARM
LED
BUZZER
Armed A
Logic equation
ALARM = A(D + W + M)
This is purely combinational: the alarm reflects the present sensor inputs.
7/9

## Slide 8
7. Simulation & Verification
Test input combinations before implementing the circuit in hardware.
Simulation inputs
D, W, M and A can be represented by switches or digital input sources.
Logic circuit
Implement OR + AND gates, then connect the outputs to LED/Buzzer indicators.
Expected result
Alarm = 1 only when the system is armed and at least one intrusion condition is active.
D
W
M
A
ALARM
Status
0
0
0
1
0
Safe
1
0
0
1
1
Door alert
0
1
0
1
1
Window alert
0
0
1
1
1
Motion alert
1
0
0
0
0
Disarmed
8/9

## Slide 9
8. ALU Connection & Key Takeaways
Making decisions and doing maths with combinational logic.
ALU — Arithmetic Logic Unit
The ALU is a major combinational block in a CPU. It performs operations such as addition, subtraction, AND, OR and comparisons based on control inputs.
Connection to Module 2
• K-maps simplify control logic • Adders perform binary arithmetic • Gates implement decisions • Ripple-carry adders build wider arithmetic units
Smart Security System — Final Design Summary
1. Sensors generate binary inputs. 2. Boolean logic combines current sensor states. 3. K-map simplification reduces hardware complexity. 4. AND/OR gates decide whether an intrusion condition exists. 5. The armed signal enables the alarm decision. 6. Simulation verifies safe and alert cases. 7. The same combinational principles scale to larger digital systems and ALU design.
Final takeaway: Current inputs → Boolean decision → Immediate output
9/9

## Slide 10
9. Conclusion
Combinational logic converts real-time sensor inputs into immediate security decisions.
Combinational Logic
The alarm depends only on the current sensor inputs.
K-Maps
Logic can be simplified to reduce gates, cost, delay and power.
Arithmetic Circuits
Half adders, full adders and ripple-carry adders demonstrate digital computation.
Smart Security
Door, window, motion and armed signals can be combined into a practical alarm system.
ALU Connection
The same combinational principles form the basis of arithmetic and logic operations in CPUs.
Final takeaway: Current Inputs → Boolean Decision → Immediate Output
10/11

## Slide 11
THANK YOU
Smart Home Security & Intruder Detection System
DONE BY — BATCH 6
Roll Numbers
2620030506 • 2620030518 • 2620030525
2620030532 • 2620030526
Questions & Discussion
11/11

## Slide 12
9. Logisim Circuit Diagram — Smart Home Intruder Detection
Combinational implementation of ALARM = A(D + W + M)
D Door
W Window
M Motion
A Armed
OR
AND
ALARM
LED
BUZZER
D
W
M
A
Intrusion
Alarm output
Logisim implementation: 3-input OR gate → 2-input AND gate • Inputs are switches • Outputs can drive LED/Output pins and a buzzer indicator
10/12